## Slide 1: 视频压缩技术 Basic Video Compression Techniques
授课教师：张小燕
邮箱：xyzhang15@szu.edu.cn
2021年春季课程

## Slide 2: 知识点回顾
Image compression standard JPEG
Block diagram for JPEG encode
  Transform RGB color model to YUV or YIQ
  DCT coding for image block
  Quantization of DCT coefficients
  ZigZag scan for quantized DCT coefficients
    DPCM for DC coefficients
    RLC for AC coefficients
  Entropy coding
  JPEG file generation

## Slide 3: Block Diagram for JPEG Encode

## Slide 4: Uniform Scalar Quantization
Motivation
  Yield higher compression ratio
  Main source for compression in JPEG
Quantize DCT coefficients
  F(u,v) represents a DCT coefficients
  Q(u,v) is a “quantization table" entry
  represents the quantized DCT coefficients

## Slide 5: Zig-Zag Scan for Quantized DCT Coefficients
Zig-Zag scan
Zigzag scan result:
(32, 6,-1,-1,0 –1,0,0,0,-1,0,0,1,0,0… … 0)
To make it most likely to hit a long run of zeros: a zig-zag scan is used to turn the 8 × 8 matrix (u, v) into a 64-vector.

## Slide 6: DPCM for DC Coefficients
Quantized DCT coefficients
  DPCM is the coding method for DC coefficients
  Differential Pulse Code Modulation （差分脉冲编码调制）
Example of encoding DC coefficients
  assuming di = DCi+1 − DCi, and d0 = DC0.
  DC coefficients for the first 5 image blocks: 150,155, 149, 152, 144
  Coding result: 150, 5, -6, 3, -8

## Slide 7: Run-length Coding (RLC, 游长编码) on AC coefficients
RLC aims to turn the (u, v) values into sets
{#-zeros-to- skip , next non-zero value}.
Zigzag scan result
(32, 6,-1,-1,0 –1,0,0,0,-1,0,0,1,0,0… … 0)
Modified Run-Length coding result
(0,6)(0,-1)(0,-1)(1,-1)(3,-1)(2,1)(0,0)

## Slide 8: 练习
1030 | 130 | -24 | 8 | 2 | 4 | -16 | 10
-32 | 6 | 4 | 0 | 0 | -22 | -4 | 6
-24 | 12 | 22 | -2 | 6 | 0 | 2 | -2
-16 | 6 | -8 | 4 | -4 | -6 | -10 | -4
0 | -4 | 14 | -10 | 8 | 0 | -2 | -8
0 | -3 | -2 | 0 | 8 | 2 | -2 | 0
6 | -4 | -6 | 6 | 6 | -2 | -2 | -6
-4 | 10 | -4 | 8 | -4 | 4 | -6 | 0
量化结果?
Z字扫描 的结果？
AC系数的游长编码？
F(u,v)

## Slide 9: 练习
64 | 12 | -2 | 1 | 0 | 0 | 0 | 0
-3 | 1 | 0 | 0 | 0 | 0 | 0 | 0
-2 | 1 | 1 | 0 | 0 | 0 | 0 | 0
-1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Z字扫描的结果？
64， 12， -3， -2， 1， -2，1，0，1，-1，0，0，1，0，…0
AC系数的游长编码？
（0,12）（0，-3）（0，-2）（0,1）（0，-2）（0,1）（1,1）（0，-1）（2,1）（0,0）
量化结果

## Slide 10: 练习
DC系数：140, 75, 90, 120, 80, 45
DC系数的DPCM 编码？
140， -65，15，30，-40，-35
表示？
（8,10001100）（7，0111110）（4，1111）（5,11110）（6，010111）（6, 011100）

## Slide 11: Outline of Lecture 10
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 12: Introduction to Video Compression
A video consists of a time-ordered sequence of frames  images
An obvious solution to video compression would be predictive coding based on previous frames
  Compression proceeds by subtracting images: subtract in time order and code the residual error

## Slide 13: Introduction to Video Compression
An obvious solution to video compression would be predictive coding based on previous frames

## Slide 14: Introduction to Video Compression
An obvious solution to video compression would be predictive coding based on previous frames

## Slide 15: Introduction to Video Compression
It can be done even better by searching for just the right parts of the image to subtract from the previous frame
Target
Reference

## Slide 16: Outline of Lecture 10
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 17: Video Compression with Motion Compensation (运动补偿)
Temporal redundancy (时间冗余) exists between consecutive (连续的) frames
  Not every frame of the video needs to be coded independently (独立的) as a new image
  The difference between the current frame and other frame(s) in the sequence will be coded.
Steps of video compression based motion compensation (MC)
  Motion estimation
  MC-based prediction
  Derivation of the prediction error

## Slide 18: Outline of Lecture 10
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 19: Motion Compensation
Each image is divided into macroblocks（宏块）of size N × N .
  By default, N = 16 for luminance images.
  For chrominance images, N = 8 if 4:2:0 chroma subsampling is adopted.
Motion compensation is performed at the macroblock level.
  The current image frame is referred to as Target Frame.
  A match is sought between the macroblock in the Target Frame and the most similar macroblock in previous and/or future frame(s) (referred to as Reference frame(s)).
  The displacement of the reference macroblock to the target mac- roblock is called a motion vector MV.

## Slide 20: Macroblocks and Motion Vector in Video Compression
MV search is usually limited to a small immediate neighborhood — both horizontal and vertical displacements in the range [−p, p].
This makes a search window of size (2p + 1) × (2p + 1).

## Slide 21: Search for Motion Vectors
Calculating the displacement of the reference macroblock to the target macroblock
Reference image
Target image

## Slide 22: Search for Motion Vectors
The difference between two macroblocks can be measured by Mean Absolute Difference (MAD)，平均绝对误差
The goal of the search is to find a vector (i, j) as the motion vector MV = (u,v), such that MAD(i, j) is minimum
(u, v) = [ (i, j) | M AD(i, j) is minimum, i ∈ [−p, p], j ∈ [−p, p] ]

## Slide 23: Mean Absolute Difference (MAD)
Reference
Target
100
10
Calculate MAD：
MAD=(|10-100|+|10-100|+7* |10-10|+7* |100-100|)/16=180/16

## Slide 24: Outline of Lecture 10
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 25: Sequential Search （顺序搜索）
P=7
N=5
-P
+P
-P

## Slide 26: Sequential Search （顺序搜索）
Sequential search: sequentially search the whole (2p+1)×(2p+1) window in the Reference frame
  The vector (i, j) that offers the least M AD is designated as the MV (u, v) for the macroblock in the Target frame.
  This method is costly — assuming each pixel comparison requires three operations (subtraction, absolute value, addition), the cost for obtaining a motion vector for a single macroblock is
  (2p+1)·(2p+1)·N2·3 ⇒ O(p2N2)

## Slide 27: Sequential Search （顺序搜索）
See demo predictionMC.m
b
d
c
a
A
B
C
D
Full-pixel position Half-pixel position
Half-pixel Prediction by Bilinear Interpolation in H.263
  思考：MV（u，v）只能为整数吗？

## Slide 28: Outline of Lecture 12
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 29: 2D Logarithmic Search
Logarithmic search: a cheaper version, which is suboptimal but usually effective
The procedure for 2D Logarithmic search takes several iterations (迭代) and is akin to a binary search
  Initially only nine locations in the search window are used as seeds for a MAD-based search
  After the one that yields the minimum MAD is located, the center of the new search region is moved to it and the step-size (“offset”) is reduced to half
  In the next iteration, the nine new locations are marked as ‘2’, and so on.

## Slide 30: 2D Logarithmic Search for Motion Vectors
The total operations per second is dropped to:
  O(log p*N2)
  每一步搜索：步长=, 最优MV，MAD

## Slide 31: Algorithm of 2D-Logarithmic Search

## Slide 32: Outline of Lecture 12
Introduction to Video Compression
Video Compression with Motion Compensation
Motion Compensation
Sequential Search
Logarithmic Search
Hierarchical Search
Reference reading
  Chapter 10

## Slide 33: Hierarchical Search （分层搜索）
Sequential search method is very costly
(2p+ 1)· (2p+ 1)· N 2 · 3 ⇒ O(p2N 2)
Reduce p and N, could reduce the cost.
The search can benefit from a hierarchical (multiresolution) approach in which initial estimation of the motion vector can be obtained from images with a significantly reduced resolution.

## Slide 34: A Three-level Hierarchical Search for Motion Vectors
Original image is at Level 0, images at Levels 1 and 2 are obtained by down-sampling from the previous levels by a factor of 2, and the initial search is conducted at Level 2.
Since the size of the macroblock is smaller and p can also be proportionally reduced, the number of operations required is greatly reduced.

## Slide 35: Comparison of Computational Cost
Search Method | OP S per second for 720 × 480 at 30 fps | 
 | p = 15 | p = 7
Sequential search | 29.89 × 109 | 7.00 × 109
2D Logarithmic search | 1.25 × 109 | 0.78 × 109
3-level Hierarchical search | 0.51 × 109 | 0.40 × 109

## Slide 36: 练习题

## Slide 37: 练习题
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
3
3
3
3
3
3
3
3
x
y